## Slide 1: Generate Blocks
“generate” statements allow Verilog code to be generated dynamically before the simulation or synthesis begins.
  Very convenient to create parameterized module descriptions.
  Example: N-bit ripple carry adder for arbitrary value of N.
Requires the keywords “generate” and “endgenerate”.
Generate instantiations can be carried out for various Verilog blocks:
  Modules, user-deﬁned primitives, gates, continuous assignments, “initial” and “always” blocks, etc.
  Generated instances have unique identiﬁer names and can be referenced hierarchically.

## Slide 2
Special “genvar” variables:
  The keyword “genvar” can be used to declare variables that are used only in the evaluation of generate block.
  These variables do not exist during simulation or synthesis.
  The value of a “genvar” can be deﬁned only in a generate loop.
  Every generate loop is assigned a name, so that variables inside the generate loop can be referenced hierarchically.

## Slide 3: EXAMPLE: Design of N-bit Ripple Carry Adder
module RCA (carry_out, sum, a, b, carry_in);
parameter N = 8;
input [N-1:0] a, b;
input carry_in;
output [N-1:0] sum;
output carry_out;
wire [N:0] carry; // carry[N] is carry out
assign carry[0] = carry_in;
assign carry_out = carry[N];
genvar i;
generate
for (i=0; i<N; i++)
begin:fa_loop
wire t1, t2, t3;
xor G1 (t1, a[i], b[i]), G2 (sum[i], t1, carry[i]);
and G3 (t2, a[i], b[i]), G4 (t3, t1, carry[i]);
or G5 (carry[i+1], t2, t3);
end
endgenerate
endmodule

## Slide 4
Implement m*n unsigned array multiplier using parameter and generate statements.